## Slide 1: Web Services
National Geospatial Management Center (NGMC)
September 27, 2012

## Slide 2: Webinar Presenter
Jennifer Sweet
  If the name Jennifer Sweet doesn’t ring any bells you may remember me as Jennifer Brookover.
  Soil Scientist with SCS/NRCS for 24 years.
  Nearly 5 years in WV before moving to NCGC/NGMC in Fort Worth.

## Slide 3: Questions?
If you have questions during the webinar please submit them using the LiveMeeting Q & A link.
Send your questions in any time during the webinar and I’ll try to leave some time at the end to answer.
If you have questions after the webinar you can send me an e-mail at Jennifer.Sweet@ftw.usda.gov
or call 817-509-3421.

## Slide 4: What exactly is a Web Service?
According to Wikipedia, “A Web service is a method of communication between two electronic devices over the World Wide Web”.
You can get data on your machine, in your office, from a computer located at NGMC (Fort Worth) over the Internet using a browser like IE (Internet Explorer).
All you need is a URL (Uniform Resource Locator).

## Slide 5: URL
If I type the following URL in a browser,
It leads me to this web service,

## Slide 6: NAIP CIR
http://ncgcws.ftw.nrcs.usda.gov/ArcGIS/rest/services/ortho_imagery/NAIP_CIR/MapServer?f=jsapi

## Slide 7: About the URL
Let’s back up a bit on the URL, from
To
Hostname
Instance
Protocol
Services

## Slide 8
The services directory allows browsing of the contents of the server and to obtain information about the services.
Version of ArcGIS
A view of the geographic catalog that can be viewed in Google Earth. It is a downloadable kmz file.
Folders on this server containing services. Expressed as themes.
(Pretend F: Geodata)
Sitemap and Geo Sitemap are Google interfaces.

## Slide 9: REST and SOAP Interfaces
These are both protocols for exchanging information through web services over a computer network.

## Slide 10: SOAP
Simple Object Access Protocol (SOAP) is a specification to exchange information using Extensible Markup Language (XML).
Advantages: versatile, uses HTTP to tunnel through firewalls.
Disadvantages: slower.

## Slide 11: REST
REpresentational State Transfer (REST) is more an architectural style that consists of clients and servers.
The client initiates requests to the server and the servers process the requests and return the appropriate response.
Advantages: lightweight, easy to build.
Disadvantages: no common standard. Up for certification at Open Geospatial Consortium (OGC).
Most common web service design is REST.

## Slide 12: Just for Fun
A quick Google search for ArcGIS/rest/services:
  http://gis.srh.noaa.gov/ArcGIS/rest/services
  http://129.79.145.13/ArcGIS/rest/services/Maps/Weather/MapServer
  http://services.nationalmap.gov/ArcGIS/rest/services/
  http://www.geocommunicator.gov/ArcGIS/rest/services/

## Slide 13: Web Services
A web service does not have to serve data that can be consumed by a GIS.
Twitter, Yahoo, Flickr, eBAY and Amazon all have web services that do not contain geospatial data.
This webinar will focus on the different types of Geospatial Web Services.

## Slide 14: Geospatial Web Services
A map is created in ArcMap (mxd) and is then published to the Web creating a web map service (WMS).
The map, from the service, can be used in Web applications, ArcMap and other applications.

## Slide 15: Web Map Service
The following URL displays this page of Folders.

## Slide 16: Folders
Each folder contains themes of web services.
There can be different types of services:
  Map
  Geoprocessing
  Image

## Slide 17: Folders
Services in the government_units folder

## Slide 18: Naming Convention
Follow the USDA-SCA Geospatial Dataset File Naming Standard.
The standard file names convey as much information as possible:
  dataset theme
  type of map features in the dataset
    Point (p), line (l), area (a)
  spatial location or extent of the dataset
  file extension (as applicable)
government_units/sca_a_us

## Slide 19: Folders
_a means polygons, _l for lines. The _us denotes a service for the US

## Slide 20: Folders
Select the map service

## Slide 21: Government_units/sca_a_us
Applications to view the service in.
The intended use for the service.
http://spatialreference.org/ref/epsg/4269/html/
GCS NAD83
Layers in this service.

## Slide 22: Government_units/sca_a_us
Units of the data
The operations that can be performed with this service.

## Slide 23: SCA Layer
A vector polygon feature layer.
Select SCA
The label that displays.

## Slide 24: SCA Layer
All the fields contained in this feature layer along with the data type and alias.
Query can be supported on this layer.

## Slide 25: What We Know about the SCA Layer
On host ncgcws in the government unit services folder.
Select sca_a_us layer:
  What applications to view the data in
  Description – District Locations
  Projection - 4269 GCS NAD83
  Supported Operations – Export, Identify, Find
  Display Field - SITE_NM
  Geometry Type - Polygon
  All fields in the layer

## Slide 26: sca_a_us Layer

## Slide 27: Adding the Service to ArcCatalog
1-Expand GIS Servers
2-Double –click Add ArcGIS Server
3-Default
4

## Slide 28: Adding the Service to ArcCatalog
5-Type URL
6-Finish
Notice rest is not part of the URL.

## Slide 29: Adding the Service to ArcCatalog
Service added to Catalog Tree
Contents tab displays folders

## Slide 30: Comparison
http://ncgcws.ftw.nrcs.usda.gov/ArcGIS/rest/services
ArcCatalog

## Slide 31: Adding the Data to ArcMap
1-Click the Add Data button
2-Select GIS Servers

## Slide 32: Adding the Data to ArcMap
3-Double-click the ncgcws service
4-Select the folder containing the service to add to ArcMap
The red “x” means the service is not connected

## Slide 33: Adding the Data to ArcMap
government_units was selected
5-Select sca_a_us
6-Click Add

## Slide 34: Adding the Data to ArcMap

## Slide 35: Supported Operations
Remember the operations supported by the service – Identify being one of those.
Identify
Identify Results

## Slide 36: Downloading Data
If you need to do more with the data than just Identify and Export, download from the Geospatial Data Gateway.
The data can be downloaded from the service also.
http://datagateway.nrcs.usda.gov/

## Slide 37: Other Data in the Services
You may run across data that have been built and altered for specific purposes.
Many times data are generalized for display speed.
This can help in locating a specific area in a US dataset quickly.

## Slide 38: Generalized Maps
The layer is described as ‘Most Generalized’
Notice the scale of 1:60 million

## Slide 39: Generalized Maps
States ‘Generalized’
Notice the scale of 1:4 million
A generalized representation of the coast.

## Slide 40: Geoprocessing Service
Contains geoprocessing tasks accessible by Web-enabled clients.
Tasks are created by publishing geoprocessing model and script tools.
Each tool in the toolbox becomes a task in the service.

## Slide 41: Geoprocessing Service
http://ngmcgp.ftw.nrcs.usda.gov/ArcGIS/rest/services/
NGMC would like to do more with geoprocessing services.
Something we will be investigating.

## Slide 42: Geoprocessing Service
What the tool is used for.
One of the requirements for a gp service is tasks.
Name of the task.

## Slide 43: Geoprocessing Task
Choose a source layer.
Add a point on the chosen source layer.

## Slide 44: Geoprocessing Task
Result

## Slide 45: Add the Geoprocessing Service
1-Add the geoprocessing service
2-Open ArcToolbox

## Slide 46: Add the Geoprocessing Service
3-Double-click on ngmcgp
4-Select Elevation Tool
5-Click Open

## Slide 47: Add the Geoprocessing Service
Elevation Toolbox is added
6-Expand the Toolbox

## Slide 48: Add the Geoprocessing Service
7-Double-click ‘Get MapService Features’
8-Input parameters to run tool

## Slide 49: Geometry Service
Helps applications perform geometric calculations such as buffering or projecting.

## Slide 50: Other Web Services
A Feature Service enables editing on a layer:
  NGMC has 1 WFS that is being tested
A Geocode Service allows for finding and displaying of addresses on a map.
There are also geodata services, globe services, KML services, mobile services supported with ArcGIS Server.
  NGMC does not offer any of these services.

## Slide 51: Hosts
The ncgcws host contains public web services.
NGMC has other hosts that you may come across.

## Slide 52: Other Hosts
http://gdwweb1.ftw.nrcs.usda.gov/ArcGIS/rest/services
http://imageserver1.ftw.nrcs.usda.gov/ArcGIS/rest/services
http://imageserver2.ftw.nrcs.usda.gov/ArcGIS/rest/services
Not an inclusive list.

## Slide 53: Services
There are approximately 200 web services at NGMC.
Some of the 200 services are duplicates:
  Still supporting ArcGIS 9.2
  Many of the ArcGIS 10 services are in the Web Mercator projection
  Web Mercator is not supported until ArcGIS 9.3.1
  A Web Mercator service will crash ArcGIS 9.2

## Slide 54: Other Hosts and Services
If the host name or service has test anywhere in the name then do not use in your map.
Some of the 200 services are tests
  Testing various options of the data and services
It can be confusing to have both test and production services on the same host
  NGMC is working on having enough room to do both production and testing on separate hosts
We are having the same experiences you are, “Doing more with less”.

## Slide 55: Image Services
Provides access to raster (and image) data.
Requires a raster or mosaic dataset.
Can be used in ArcGIS Desktop.
There are approximately 100 image services at NGMC.

## Slide 56: Map vs. Image Service
A map service requires an mxd.
An image service does not.
Serving image (raster) data through a map service requires an mxd
  This will slow the rendering of imagery data
  This will not slow the rendering of vector data
Serving image data through a image service does not require an mxd, can consume directly
  This will speed the rendering of the data
Old (map service) vs. new (image service).

## Slide 57: Image Service
In order to use the image service in ArcMap the Image Server Plugin must be installed in ArcGIS 9.2 and 9.3.

## Slide 58: Image Server Plugin
The image server plugin is available for download and installation for ArcGIS 9.2 and 9.3:
  It is CCE Certified
  There are separate plugins for 9.2 and 9.3
  Contact your local ITS
The plugin is provided in ArcGIS 9.3.1 and 10.0.

## Slide 59: Adding the Plugin to ArcMap 10
1-Select Customize
2-Select Customize Mode
3-Select Commands
4-Select Image Server
5-Select Add Image Server Connection

## Slide 60: Adding the Plugin to ArcMap 10
6-Left click and drag to ArcMap toolbar
7-Release left mouse button
8-Close

## Slide 61: Adding Image Service Data to ArcMap
1-Select Add Image Server Connection button
2-Type imageserver1.ftw.nrcs.usda.gov:10010
3-Click Get Services
Services available on imageserver1

## Slide 62: Adding Image Service Data to ArcMap
4-Expand
6-Add
Can add more than one service at a time, just keep selecting and adding.
7-OK
5-Select

## Slide 63: Adding Image Service Data to ArcMap

## Slide 64: Map vs. Image Service
A map service requires an mxd.
An image service does not.
Serving image (raster) data through a map service requires an mxd
  This will slow the rendering of imagery data
  This will not slow the rendering of vector data
Serving image data through a image service does not require an mxd, can consume directly
  This will speed the rendering of the data
Old (map service) vs. new (image service).

## Slide 65: Image vs. Map Service
Images served through a map service on ncgcws.
A map service because it requires a mxd.
Renders more slowly for imagery data not vector data.
The map services are used mainly to support those clients in ArcGIS 9.2.

## Slide 66: Image vs. Map Service
Images served through an image service on imageserver1.
An image service because it does not require an mxd.
Renders faster.

## Slide 67: Image vs. Map Service
Map Service
Image Service
Same data

## Slide 68: What’s Coming
In ArcGIS 10.1 image server is being replaced by something called mosaic datasets:
  More testing services will appear when NGMC begins implementing
  More duplicate services also to continue supporting ArcGIS 9.2, 9.3, and 10.0

## Slide 69: Caching Service
A map cache is the entire map at several different levels or scales.
The cache also stores the copies of the map images.
Map caching is a very effective way to make maps and applications run faster.
It can take a while to create the cache but the benefits are performance and quality.

## Slide 70: Caching Service
A cache tiling scheme must be created.
The cached images are no longer in a GIS format, instead they become a picture in either JPEG or PNG format.
JPEG usually used for imagery.
PNG format is used for any feature that requires transparency (opacity).
A service can have a mix of JPEG and PNG formats.

## Slide 71: Levels of Caching
Most of the image services have approximately 14 to 18 levels.
The levels can differ depending on the data and the intended use of the data.

## Slide 72: Cached Maps
Back to ncgcws.ftw.nrcs.usda.gov. Select easements.
Select

## Slide 73: Cached Maps
A good description of the service.
Imagery from 2007.
Spatial Reference 4326=WGS84

## Slide 74: Cached Maps
9 levels of detail.
Each level has a scale.
Format = Mixed (Both JPEG and PNG).

## Slide 75: Cached Maps
The NAIP imagery collection:
  Entire US
  The year is not important as not every state is collected each year
  4 band
  1 meter resolution
  35 terabytes (TB) of raw data
    1 terabyte = 1024 gigabyte

## Slide 76: Cached Maps
Each increase in levels or scale (ex: 24,000 to 12,000) increases the storage by a factor of 4.
Also increases the time to produce by 4.
It takes 4 times longer to produce caches at 12,000 than 24,000 and takes 4 times the storage space to store tiles at 12,000 than 24,000 scale.
Another way to describe ‘cost’.

## Slide 77: Cached Maps
Caching allows for the data to be compressed
  35 TB to 4 TB with caching
4 TB includes 17 levels with the final level at 1.2 meter resolution.
However, 4 TB of NAIP + 4 TB of NAIP CIR.
Still, 8 TB is less than 35 TB.

## Slide 78: How Do We Remember All These Hosts?
Instead of trying to remember all the different URLs NGMC has tried to collect all the services in one spot – GeoPortal:
  http://ncgcweb.ftw.nrcs.usda.gov/geoportal/catalog/main/home.page
  Allows searching by theme
GeoPortal is a work in progress
  Doing more with less

## Slide 79: GeoPortal

## Slide 80: GeoPortal
Select Data Themes
Select State Boundaries Map Service

## Slide 81: GeoPortal
Select Open

## Slide 82: GeoPortal
Select Preview

## Slide 83: GeoPortal
Select Details

## Slide 84: GeoPortal
Select Metadata

## Slide 85: Web API
A web API (Application Programming Interface) is a set of HTTP requests along with responses usually expressed in XML.
The advantage of a web API allows for the combination of multiple services into a new application known as a mashup.
Microsoft Silverlight is an example of an API.

## Slide 86: Web API
Very quick to stand-up.
NGMC uses Silverlight to supply imagery for disaster areas.
In 2011 Hurricane Irene, Mississippi and Missouri River Flooding.
The services will be turned off eventually.
Only available within the USDA network.

## Slide 87: Missouri River Disaster Service

## Slide 88: Missouri River Disaster Service
Check for Visible
Transparency Slider
Imagery on different dates

## Slide 89: Missouri River Disaster Service
A list of all the layers in the service

## Slide 90: What’s Coming for Services
Elevation (LiDAR) Services
  6 TB of data and growing daily
Do it yourself, publish your own web service
  We hope – doing more with less

## Slide 91: Future Plans for the Services
The services are currently hosted at NGMC.
All the services will move within the next year.
Yes, the URLs will change and there isn’t any way to prevent that.
Why?

## Slide 92: Federal Data Center Consolidation
Fort Worth data center is scheduled to close at the end of 2013 fiscal year:
  This is not the same as the National Geospatial Management Center
  The Fort Worth office is not closing
  Only the data center (hardware, software, services) are closing
For more information about the Federal Government Data Center Consolidation Initiative visit
  https://explore.data.gov/Federal-Government-Finances-and-Employment/Federal-Data-Center-Consolidation-Initiative-FDCCI/d5wm-4c37?

## Slide 93: Where are the Web Services Moving to?
Most likely the National Information Technology Center (NITC) in Kansas City.
http://www.ocio.usda.gov/nitc/index.html
Why here and not somewhere commercial?
The answer to that is FISMA.

## Slide 94: FISMA
Federal Information Security Management Act of 2002 (FISMA).
Recognizes the importance of information security.
“Requires each federal agency to develop, document, and implement an agency-wide program to provide information security for the information and information systems that support the operations as assets of the agency, including those provided or managed by another agency, contractor, or other source.”

## Slide 95: FISMA
Defines 3 levels of potential impact on organizations or individuals should there be a breach of security.
The impact levels are low, moderate and high.
OCIO must make a determination of the impact level of your data.
The storage solution provider must have matching certification
  If the data have moderate potential impact the storage provider must be FISMA moderate certified

## Slide 96: FISMA
OMB requires government data to be stored at a FISMA certified location
  It’s called Authority to Operate (ATO)
Currently only 3 FISMA certified locations:
  NITC in Kansas City
  NFC in New Orleans
  NASA (I’m not sure where)

## Slide 97: FISMA
The law requires each federal agency to develop, document…
Yes, Amazon and Google cloud services may be FISMA certified, but for what Agency?
Amazon had FISMA certification, but for only one Agency and only on one application.
The certification has since expired.

## Slide 98: FISMA
Unfortunately, we cannot make commercial solutions become FISMA certified.
It may not be in their business model to jump through all the government hoops.

## Slide 99: FedRAMP
Federal Risk and Authorization Management Program is a government-wide program that provides a standardized approach to security assessment, authorization, and continuous monitoring for cloud products and services.
Trying to get away from each Agency shall…
Making progress, but slowly.

## Slide 100: What is a Cloud?
The use of hardware and software resources that are delivered as a service over a network, usually the Internet.
Clouds usually use REST-based APIs.
Several types of cost models.
Commercial vendors usually provide only racked storage and the customer provides much of the other services.

## Slide 101: Cloud Services
Cloud services require:
  Storage pricing
  Data transfer pricing:
    Adding NAIP 2013, new LiDAR data, etc.
    Data are not static
  Backing up the data
  Who patches for Security vulnerabilities?
  Not an inclusive list

## Slide 102: An Exercise
Amazon pricing
  First TB/month $0.125 per GB
  Next 49 TB/month $0.110 per GB
NITC pricing
  $0.88/month per GB
1 TB = 1024 GB
4 TB of NAIP = 4096 GB
  1024 * $0.125 + 3072 * $0.110 = $466/month * 12 = $5591/year (Amazon)
  4096 GB * $0.88 = $3604/month * 12 = $43238/year (NITC)

## Slide 103: An Exercise
4 TB NAIP + 4 TB NAIP CIR + 6 TB LiDAR = 14,336 GB * $0.110 = $1,576/month * 12 = $18,912/year
14,336 GB * $0.88 = $12,615/month * 12 = $151,388/year
14 TB is not all the data!
This is only the storage cost and does not include other costs.
Please note that these prices change regularly and were accurate as I knew them on 9/27/2012. Prices may be different tomorrow.

## Slide 104: Make a Map from Services
Select Add Basemap
Select Imagery
Click Add

## Slide 105: Make a Map from Services

## Slide 106: Make a Map from Services
Turned on Boundaries and Places
I zoomed in while you weren’t looking.

## Slide 107: Make A Map from Services
Select Add Data from ArcGIS Online
Click Add
Searched for soils

## Slide 108: Make A Map from Services
Zoomed in a little more
Added a Soils service from ESRI that displays the Dominant Order
The Fort Worth Federal Center Building 23 National Geospatial Management Center.
Can you see me waving BYE?!

## Slide 109: Got Questions?
Send them in via the LiveMeeting Q & A link.
Jennifer.Sweet@ftw.usda.gov
817-509-3421